  - Material:

1.0mm thick Bondek II galvanized steel cold form decking with the following specification.

Material Thickness: 1.0mm

Material Grade: AS 1397 G550 with yield strength= 550N/mm2 and Tensile strength= 550N/mm2

Corrosion Protection Coating:  Z275 or SuperDyma  (Zinc+ Alum. Alloy) Coating

Complying Standard: Australian Standard 1397 & BS EN 10147.